MeltonCraft™ Non-Tapered Column Cover Installation Instructions

Warning: the precision machined edges of MeltonCraft CPVC column components can be extremely sharp. Use of appropriate personal protection equipment is required: wear gloves when handling the product, wear a dust mask when cutting the product, and always wear eye protection.

Use of polyurethane adhesive, such as Gorilla Glue®, Loctite® PL Premium® Adhesive, Christy’s™ Clear PVC Pipe Cement (or other clear PVC cement), or similar products is recommended. Always observe adhesive manufacturer’s instructions.

Assembly is easiest with pneumatic or electric pin-nailers. These should recess the head of the pin nails far enough that only a minor touch-up is necessary (touch-up with caulk prior to painting.)

- Measure overall opening from floor to beam or soffit (must have structural pressure-treated post or lally column for load support.)

- Install blocking around load bearing post (use pressure treated lumber.) Final width of blocking must be same width as inside of column.

- Install blocking around center and top of post to match step 2 (center blocking is optional.) Blocking may be attached to deck/soffit instead of post if necessary.

- Trim shaft pieces at least ¼” shorter than opening height (from step 1). Trim ONLY from the bot- tom—top end is marked.

7) Using finish nails, assemble three panels together. Observe joint diagram on reverse to determine correct nail placement.

5) Lay 3 panels flat and apply ad- hesive to center joints.

8) Place the partially assembled (three panels) column around post and blocking.

6) Assemble three panels as shown.

- Apply adhesive to fourth panel and assemble to shaft. Pin-nail in place, nailing as per joint diagram on reverse.

- Screw or nail column to blocking ONLY ON THE BOT- TOM. Do not attach at center or top (to allow for expansion).

13) The TOP of the shaft should NOT be fastened to the blocking, and there should be at least ¼” gap to allow expansion (see step 4).

16) Option 2: Leave ¼” expansion room above cap, and pin-nail the cap to the column. Be sure the pin-nails DO NOT reach the blocking inside!*

11) Apply adhesive to mitered edges of base moulding (standard base is 9¼” tall) and assemble around bottom of column shaft.

14) There are TWO methods of attaching the cap. First, apply adhe- sive to mitered edges of cap mould- ing (7¼” tall) and assemble around shaft and pin-nail joints.

17) Caulk edges of base, cap, and nail holes.

12) Fasten joints on base with pin- nails.

15) Option 1: Attach cap to soffit with construction adhesive and toe- nail to soffit. DO NOT ATTACH cap to column shaft if the cap is flush with soffit (to allow expansion).*

- Clean surface of column with cleaner recommended by the paint manufacturer. Paint with 2 coats of acrylic latex paint.

Please note the correct assembly of the mitered joint shown at the left. Nails MUST be installed only in the edg- es shown (3 and 4). Installing on the other edges may re- sult in open seams.

  - Glue both joint edges; slide first joint together

  - Push second joint closed

  - Nail this joint first

  - Nail this joint second

Notes:

Panels are marked “TOP” — trim from the bottom only. Cap and base pieces are also marked as “CAP or “BASE” Only use non-corrosive fasteners — galvanized, stainless steel, etc.

Always follow glue and paint manufacturer’s instructions.

*Column must not be allowed to collect water, debris, etc. If the top of the column extends beyond the soffit/beam, the cap must be flashed with lead, copper, aluminum, etc. to prevent entry of water or foreign materials.