MeltonCraft™ CPVC Pedestal or Newel Post Cover Installation

Warning: the precision machined edges of CPVC column components can be extremely sharp. Use of appropriate personal protection equip- ment is required: wear gloves when handling the product, wear a dust mask   when cutting the product, and always wear eye protection.

Use of polyurethane adhesive, such as Gorilla Glue®, Loctite® PL Premium® Adhesive, Christy’s™ Clear PVC Pipe Cement (or other clear PVC ce- ment), or similar products is recommended. Al- ways observe adhesive manufacturer’s instruc- tions.

Assembly is easiest with pneumatic or electric pin- nailers. These should recess the head of the pin nails far enough that only a minor touch-up is necessary (touch-up with caulk prior to painting.)

Installers should read the installation instructions for CPVC column covers in addition to this docu- ment for more information (joints, etc.)

3) Apply polyurethane glue to both edges of ONE PANEL only.

6) Slide the three-panel shaft unit over the blocking, then attach. Apply glue to exposed vertical edges of panels.

9) Note: top platform usually extends be- yond top of shaft section (not shown in photo). Mouldings are applied under the  top platform. Assemble top platform on top of shaft. Glue mitered edges, and attach with pin-nails. (Pyramid caps do not use top platform.)

1) Install blocking around load bearing support (typically pressure treated post). Blocking should be made from pressure treated wood, and must be the same size as the inside of the ped- estal/newel.

4) Assemble two panels to glued edges of panel from step 3.

7) Glue and attach final panel. For use as a newel, additional blocking should be added between panels and post (post would be cut off at height of shaft.)

10) Apply glue to backs and mitered edges of cap moldings, then assemble to shaft below top platform with pin-nails. (Mouldings, panels, trim, and top platforms may vary from photos depend- ing on product styles.)

2) Smooth pedestals may be cut to shorter lengths if needed.

5) Pin-nail the three panels together into one unit. See column cover instructions!

8) Apply glue to backs and mitered edges of base moldings, then assemble to bottom of platform (same as no-taper column bases).

11) Caulk all seams, fill all nail holes, and clean surfaces with cleaner recommend- ed by paint manufacturer. Finish with two coats of acrylic latex paint.

Melton Classics, Inc. * PO Box 465020 * Lawrenceville GA 30042 * 1-800-963-3060 * www.MeltonClassics.com